## Slide 1
Theory of Change · Shade and Sponge: trait-based street-tree placement for heat and runoff
RT · Assignment 2 · MaCAD thesis · 4 Nov 2026
Barcelona street-tree planning decides which species goes where from measured heat (UTCI) and runoff benefit, not only how much of each species.
Today the tree master plan sets species quotas city-wide and quantifies neither heat nor runoff.
Porta (Nou Barris): canopy cover 20.1% vs the city's 30% target; plane trees ≈29% of that canopy.
WHAT IS THE CHANGE I WANT TO CREATE?
shade_sponge: an open-source Python method and tool. It scores candidate species × positions on one site from LiDAR crowns, terrain (D8 water flow), sun and design storms, then optimises the layout under the city's own rules (15% species cap, sidewalk width → tree size).
Two front-ends: Grasshopper for computational designers, a web app for planners.
Validated in Porta (Barcelona); Florence / Mataró as transfer test.
TRL ≈ 3–4: proof of concept in simulation.
OUTPUT
Technological: designers compare layouts (S0–S4) in hours instead of one manual Ladybug run per option.
Environmental: the trade-off of each tree position becomes visible: summer shade (benefit), winter shade (cost), runoff.
Scientific: an open, reproducible method; every parameter is sourced or marked as an assumption.
Impact level: demonstrated early (simulation + designer feedback).
SHORT-TERM OUTCOMES (thesis)
Industrial: landscape and design studios use the tool in public-space projects and tenders.
Governance / economic: the municipal tree department uses the outputs to justify replacement choices and green budgets with numbers.
Replication: a second Mediterranean city runs with only a new data adapter.
Impact level: expected (reasoned pathway, not yet tested).
MEDIUM-TERM OUTCOMES (1–3 yrs)
Environmental: lower street UTCI on hot days; less pluvial runoff to the sewers; more species diversity.
Social: heat relief in dense neighbourhoods where people walk and wait outdoors.
Economic: green vs grey drainage decisions argued with numbers.
Practice: trait-based placement becomes standard in Mediterranean tree master plans.
Impact level: potential.
LONG-TERM IMPACT (3–10+ yrs)
The LiDAR crown / LAI proxy is good enough (no independent LAI data to check it yet).
The fast heat proxy ranks layouts the same way as Ladybug UTCI.
SCS-CN + canopy interception (1.75 mm per unit LAI, calibrated on Anys & Weiler 2024) holds at 1 m street scale.
Trait data exist for the candidate species.
New trees reach the modelled crown size.
Designers and the city will adopt a recommendation tool.
ASSUMPTIONS
False precision: model results read as measured facts in public decisions.
Homogenisation: everyone plants the same 'optimal' species.
Healthy trees felled early because the model ranks them low.
Gains oversold: tree effects are small next to grey drainage in big storms.
Equity: optimising hotspots may leave other streets behind.
Data licences (non-commercial or unknown) limit reuse; the tool may age fast.
RISKS
Δ mean UTCI, 12–17 h, hot design day, vs S1 (the city's own replacement rule = ex-ante baseline).
Δ runoff volume and peak for the design storm vs S1.
Rank agreement: fast proxy vs Ladybug UTCI.
Runtime per scenario.
Share of layouts that meet all city rules.
Designer usability score (qualitative → 1–5 scale).
POTENTIAL INDICATORS
Number of studios / projects using the tool.
Municipal decisions or reports that cite its outputs.
Days to set up a new city (data adapter).
Transfer test: proxy vs Ladybug agreement in Florence / Mataró.
Open-source use: forks, issues, downloads.
POTENTIAL INDICATORS
Porta canopy cover: 20.1% today → city target 30% (benchmark).
Share of the dominant species vs the city-wide 15% cap.
Measured summer street temperature / UTCI before vs after planting.
Pluvial flooding incidents and complaints.
Species diversity (Shannon index).
Note: beyond the thesis timeframe.
POTENTIAL INDICATORS